## Slide 1
Conveyor-Fed Automatic PCB Test Station — System Flow Diagram
SmartBU / XNF I460 | BMW MAE Project 032080790003 | Conveyor_AutoLoader_Fixture_BOM_Rev1.0 | Charan Singh | 11.05.2026
A — Station State Machine (Operational Flow)
1 IDLE
Conveyor runs Light: YELLOW
2 PCB ARRIVING
Entry sensor triggered
3 PCB POSITIONED
Centre sensor confirmed
4 BARCODE SCAN
Scanner reads DataMatrix
5 PRESS CLOSING
Cylinder extends Pogopin contact
6 CONN. MATING
3× connector cylinders extend
7 TESTING
orchestrator.py full test seq.
8 PRESS OPENING
Connectors then press retract
9 RESULT OUTPUT
PASS→main line FAIL→reject tray
10 LOGGING
MySQL write HTML report
11 IDLE (reset)
Returns to IDLE state
12 FAULT
E-stop / curtain breach / timeout
timeout / invalid
low pressure / operator reset
Idle / Ready
Hardware Action
Decision / Branch
Test Instruments
Software / Logging
Fault / Safety
State 6 — CONNECTOR MATING detail
After press plate lands: 3 pneumatic cylinders (Ø16mm) extend sequentially. DO0.3 → DO0.4 → DO0.5. Press FIRST, then connectors. Settle: 0.5 s.

## Slide 2
Conveyor-Fed Automatic PCB Test Station — System Architecture
SmartBU / XNF I460 | BMW MAE Project 032080790003 | Conveyor_AutoLoader_Fixture_BOM_Rev1.0 | Charan Singh | 11.05.2026
B — System Architecture (mapped to System Overview )
UPSTREAM CONVEYOR
Belt 600mm · 24VDC
[States 1-2]
PCB STOPPERS
Entry + Exit (Ø10mm cyl.)
[State 3]
BARCODE SCANNER
2D DataMatrix · USB HID
[State 4]
PRESS STATION
Ø80mm cyl. + pogo carrier
[States 5-8]
EXIT / REJECT GATE
PASS→main FAIL→tray
[States 9-10]
PNEUMATIC PRESS (BOM §2-§5)
• Cylinder Ø80mm, ~500N @ 5 bar (item 6) — 5/2 solenoid valve • Top press plate + pogo-pin carrier (29 pins) (items 8, 23-24) • 3× Connector plug-in cylinders Ø16mm (item 26) • FRL unit + pressure sensor + flow control (items 15-17)
TEST INSTRUMENTS (BOM §8)
• KIKUSUI PWR401L — 12V / 3.8V DC supply to DUT • Lauterbach Trace32 — SWD/JTAG firmware flash + debug • PEAK PCAN-USB — CAN-H / CAN-L bus • PLIN-USB — LIN bus communication with DUT
TEST PC (BOM §10) — orchestrator.py
• orchestrator.py — sequences PSU→Flash→CAN→LIN→Motor→EOS→NFC • gui_main.py | barcode_utils.py | trace32_adapter.py • can_service · lin_service · motor_service · nfc_service • MySQL client — logs result, barcode, variant, time | HTML report
PASS → Exit Conveyor
Light GREEN · DO1.0 ON
FAIL → Reject Tray
Light RED · DO0.6 GATE
PLC CONTROL UNIT (BOM §6)
Siemens S7-1200 1214C DC/DC/DC 14 DI / 10 DO / 2 AI (24VDC) DO → Solenoid valves (press + stoppers + connector actuators) DO → Reject gate · Conveyor run DO → Tower light (R/Y/G) + Buzzer DI ← Photoelectric sensors (×2) DI ← Cylinder reed sensors (×2) DI ← Light curtain OSSD DI ← E-stop NC · Air pressure OK Ethernet → HMI | Ethernet → Test PC
Arrow legend:
Solid → PCB / signal flow direction (main process path)
Green dashed → PLC control signal
Red dashed → Safety enable condition (press BLOCKED until all safety conditions met)