## Slide 1
Objective
PEAK-System stack:
Hardware: PCAN-USB (or PCAN-USB FD) for CAN, plus PLIN-USB for LIN
Software: PCAN-Explorer + PLIN-View Pro
Automation: PCAN-Basic API + PLIN API (we can script test sequences and verdict logic)
Much cheaper than CANoe licenses
Stable USB interfaces for production benches
Good API support for automated EOL testing
Easier to deploy on multiple stations
EOL Requirements:
Reliable CAN and LIN communication at line tact time.
Automated pass/fail execution and report export.
Low setup effort for multiple stations.
Stable long-run operation in factory environment.
Low total cost of ownership (hardware + software + maintenance).

## Slide 2
Comparison view for decision (EOL PCB testing: CAN + LIN)
Criteria | Kvaser Hybrid 2xCAN/LIN | PEAK PCAN-USB Pro FD | Verdict
Core fit for EOL (CAN + LIN) | Strong | Strong | Tie
CAN FD readiness | Available depending on exact variant/toolchain usage | Native CAN FD support focus in product line | Slight edge: PEAK
LIN support for production use | Good | Good | Tie
Automation/API integration | Very good (CANlib ecosystem) | Very good (PCAN-Basic + LIN APIs) | Tie
Ease of multi-station rollout | Good | Very good (commonly cost-efficient replication) | Edge: PEAK
Software/tooling cost impact | Moderate | Usually lower overall bench cost | Edge: PEAK
Risk of migration from CANoe | Low-medium | Low-medium | Tie
Best use case | If existing Kvaser ecosystem is already validated | If cost-optimized rollout is priority | Context-based

## Slide 3
Design with PEAK
PEAK PCAN-USB Pro FD as the bench-side bus interface between the test PC and the DUT (Device Under Test). The PC runs existing GUI, automation
logic, and report generation. PEAK is used only for bus communication, stimulation, and reception on CAN/LIN.
Test PC / Laptop
J-Link/T32 Service
- flash firmware
- reset / run
- read test vars
- write test vars
PEAK Bus Service
CAN Tx / Rx
LIN Tx / Rx
timing check
payload validation
SmartBU automation runner
J-Link /T32
PEAK PCAN-USB Pro FD
DUT: SmartBU PCB
Device Under Test
USB
USB
JTAG
CAN/LIN
1. Test PC
Runs your GUI project.
Executes automation flow.
Stores logs and PASS/FAIL reports.
2. J-Link / Trace32
Flashes firmware into the DUT.
Resets, halts, and runs the DUT.
Reads/writes a limited set of test firmware variables.
3. PEAK PCAN-USB Pro FD
Replaces CANoe for production communication testing.
Sends and receives CAN and LIN frames.
Verifies actual bus behavior of the DUT.
4. DUT
The SmartBU PCB being tested on the EOL bench.

## Slide 4
Design KVASER
PEAK PCAN-USB Pro FD as the bench-side bus interface between the test PC and the DUT (Device Under Test). The PC runs existing GUI, automation
logic, and report generation. KEVASER is used only for bus communication, stimulation, and reception on CAN/LIN.
Test PC / Laptop
J-Link/T32 Service
- flash firmware
- reset / run
- read test vars
- write test vars
Kvaser Hybrid 2xCAN/LIN
-CAN Tx / Rx
-LIN Tx / Rx
-timing check
-payload validation
SmartBU automation runner
J-Link /T32
Kvaser CANlib/LINlib integration
DUT: SmartBU PCB
Device Under Test
USB
USB
JTAG
CAN/LIN
1. Test PC
Runs your GUI project.
Executes automation flow.
Stores logs and PASS/FAIL reports.
2. J-Link / Trace32
Flashes firmware into the DUT.
Resets, halts, and runs the DUT.
Reads/writes a limited set of test firmware variables.
3. Kvaser CANlib/LINlib integration
Replaces CANoe for production communication testing.
Sends and receives CAN and LIN frames.
Verifies actual bus behavior of the DUT.
4. DUT
The SmartBU PCB being tested on the EOL bench.